## Slide 1: Study of Spatial Structure of a Squeezed Vacuum Field
Ph. D Defense
Mi Zhang
Advisor: Eugeniy E. Mikhailov
March 20 2017

## Slide 2: Outline
Motivation
Introduction
Correlation of self focusing and squeezing
Multi-mode structure of a squeezed vacuum field
Optical depth and its influence on squeezing
Pump shape and LO shape
Observation of beam noise
Conclusion

## Slide 3: Squeezed field
Coherent State
Standard Quantum Limit
Squeezed State
Squeezed Quantum Noise
Quantum Fluctuations in Light field:
Precision measurements
-Magnetometer
-LIGO
Quantum imaging
Quantum information
Squeezed Vacuum State

## Slide 4: Why one should care about squeezed field
Precision measurements
-Magnetometer
-LIGO
Quantum imaging
Quantum memory

## Slide 5: Polarization self rotation effect
For linearly polarized light, the orthogonal
polarization gets squeezed.
Elliptically polarized light
rotates by
Predictions of the PSR-generated squeezing in the Rb atomic vapor : - 8 dB
Current best : - 3 dB
A. B. Matsko, I. Novikova, G. R. Welch, D. Budker, D. F. Kimball, and S. M. Rochester
Phys. Rev. A 66, 043815 – Published 30 October 2002
S. Barreiro, P. Valente, H. Failache, and A. Lezama
Phys. Rev. A 84, 033851 – Published 28 September 2011

## Slide 6: Homodyne Detection scheme

## Slide 7: Experimental setup
SMPM fiber single-mode polarization-maintaining fiber
half-wave plate
GP Glan-laser polarizer
PBS polarizing beam splitter
PhR phase-retarding wave plate
BPD balanced photodetector
Parameters affect squeezing:
Pump beam intensity
Beam size
Atomic density of medium
Beam focus position in the cell

## Slide 8: Experimental setup
SMPM fiber single-mode polarization-maintaining fiber
half-wave plate
GP Glan-laser polarizer
PBS polarizing beam splitter
PhR phase-retarding wave plate
BPD balanced photodetector
Parameters affect squeezing:
Pump beam intensity
Beam size
Atomic density of medium
Beam focus position in the cell

## Slide 9: Spatial modes of light
Hermite Gaussian modes
Laguerre Gaussian modes
Figure source: Wikipedia page-Gaussian beam

## Slide 10: Self-focusing of beam
A nonlinear process in medium,
caused by the intensity distribution change in strong field

## Slide 11: Correlation between self squeezing and squeezing

## Slide 12: Interferometric scheme of detection
To calibrate a good mode match, we introduce a parameter visibility
Usually in similar detecting scheme, a visibility of 90% is necessary to detect squeezing.
We had V = 98%, but no squeezing was observed.

## Slide 13: Circular beam mask

## Slide 14: Circular beam mask

## Slide 15: “Telescope”

## Slide 16: Iris transmission fixed
Guoy Phase ,
has a shift across the focus

## Slide 17
Theoretical explanation
Figure credit: R. N. Lanning

## Slide 18: Theoretical explanation
Multi-mode field generated in the vapor cell, resulting in a bad mode match and less effective detection of squeezing.
M Zhang, RN Lanning, Z Xiao, JP Dowling, I Novikova, EE Mikhailov
Physical Review A 93 (1), 013853

## Slide 19: Iris size fixed

## Slide 20: Optical depth study – multipass

## Slide 21: Squeezing dependence on optical depth
P = 11 mW
Squeezing = -2.1 dB
P = 11 mW
Squeezing = -2.6 dB
P = 11 mW
Squeezing = -2.4 dB

## Slide 22: Squeezing dependence on optical depth

## Slide 23: Two cells

## Slide 24: Entangled position

## Slide 25: Spatial light modulator
A reflective device that changes the phase retardation of light incident on screen.
Yao, A.M., and Padgett, M.J. (2011) Orbital angular momentum: origins, behavior and applications. Advances in Optics and Photonics, 3 (2). p. 161. ISSN 1943-8206

## Slide 26: Change beam shape with SLM-phase modulation

## Slide 27: Change of pump
The SLM changes the pump beam shape to generate different amount of noise suppression.
Squeezing is detected by the spectrum analyzer and sent to the optimization algorithm to decide how to modify the phase mask.

## Slide 28: Feedback loop and Optimization algorithm
Optimization algorithm – Metropolis
If squeezing is improved, accept change
If not, accept change with a probability
Phase mask applied to the SLM is composed of N higher modes
with l = 0 or p = 0
is the real coefficient of the ith mode and is the imaginary part.
is the phase applied to a certain position (x, y), is the phase of the ith mode with waist w.

## Slide 29: Optimized squeezing
Original squeezing = -2.0 dB
Original squeezing = -0.7 dB
Improved squeezing = -2.3 dB
Improved squeezing = -1.2 dB

## Slide 30: Change of Local Oscillator
Original squeezing = -1.8 dB
Squeezing with SLM on = -1.0 dB

## Slide 31: Direct observation of beam
Camera: Princeton Instruments PIXIS
Attenuator : neutral density filters

## Slide 32: Noise calibration in a coherent beam
Averaged photon number
Normalized photon number noise
For coherent beam, there should be =
Figure credit: K. T. Kutzke

## Slide 33: Noise statistics
Figure credit: K. T. Kutzke

## Slide 34: Noise in a local oscillator

## Slide 35: Squeezed field
Averaged photon number
Normalized photon number noise
The normalized noise map has a clear spatial structure.
Figure credit: K. T. Kutzke

## Slide 36: Noise structure in a squeezed vacuum field
Figure credit: K. T. Kutzke

## Slide 37: Conclusions
We are able to produce -2.7 dB of squeezing below shot noise
The squeezed vacuum field generated in hot Rb vapor is in a multi-mode structure
The optical depth of medium is not the only factor that determines squeezing
Pump beam shape influences the squeezing generated in the medium, and is possible to improve it.
With a quantum noise limited camera, we can see a spatial dependence of noise in the squeezed vacuum field.

## Slide 38: Acknowledgment
Jonathan P. Dowling
R. Nicholas Lanning
Zhihao Xiao
Quantum Optics Group @ College of William and Mary
This project is supported by AFOSR grant FA9550-13-1-0098.
Louisiana State University